## Slide 1
YC Weather Pipeline Audit
Before weather-domain augmentation
•
Scope stays YC/YCA only
•
No PPO algorithm, reward, action-space or network change
•
Goal: identify the current weather source and seed contract before any augmentation run
YC weather audit | 1
Notes: Source: docs/yc_weather_pipeline_audit.md and results/yc_weather_audit/yc_weather_reset_diagnostic.json.

## Slide 2
Current YC Weather Mechanism
•
Training entry: src/055_yca_lowIC_site_transfer/run_055_00_yca_lowIC_expanded_action_maskableppo.py
•
Actual gym env_args set random_weather=false
•
Episode variation comes from sampling historical train years, not WGEN-generated weather
•
YC lowIC input directory contains historical CNYC year WTH files and no CLI file
YC weather audit | 2
Notes: The installed gym_dssat_pdi version is 0.0.5. The DssatPdi signature supports random_weather and auxiliary_file_paths, but the current env_args disable random weather.

## Slide 3
Reset Evidence
Fixed seed 0 year sequence
2012, 2010, 2009, 2006, 2007, 2004, 2004, 2004, 2005, 2012, 2010, 2013
Repeat with seed 0
The same sequence is reproduced
Real gym reset probe
First three active_year values: 2012, 2010, 2009
YC weather audit | 3
Notes: Command: docker exec -w /workspace nifty_taussig /opt/gym_dssat_pdi/bin/python scripts/diagnose_yc_weather.py --episodes 12 --gym-reset --gym-resets 3.

## Slide 4
Audit Risks
•
random_weather defaults to true inside gym-DSSAT, so every project runner must record the explicit runtime value
•
ppo_seed and weather-year sampling seed are currently coupled
•
No current YC CLI file means WGEN augmentation still needs a parameter-estimation step
•
Historical CLI files elsewhere in the repo do not prove current YC WGEN use
YC weather audit | 4
Notes: These risks affect interpretation and next-run design. They do not invalidate the current historical-weather PPO runs.

## Slide 5
Next Fair Comparison
baseline_weather
Current historical YC train-year WTH sampling, random_weather=false
augmented_weather
YC training-period weather augmentation with episode-level weather manifest
Keep fixed across both
•
PPO, reward, observation, action grid, constraints, training steps and evaluation years
•
Train weather parameters estimated only from train years
•
Validation and test true weather remain independent
YC weather audit | 5
Notes: Use seed-level reporting: yield, irrigation, fertilizer, WP_ET when replay evidence exists, PFP_N, violations, reward, timing summary, success seeds over total seeds.